# 11 13 010Removing and installing/replacing upper oil sump section (S63T 0)

|  | Special tools required: 11 9 240 11 8 780 11 4 470 |
| --- | --- |

|  | Necessary preliminary work: Drain off engine oil Lower front axle Remove lower oil sump section Remove oil pump. Release supply/return lines on oil filter Release holders of supply/return lines on oil sump Detach plug from oil pressure switch Unclip wiring harness on oil sump |
| --- | --- |

|  | Release oil filter cover (1) with special tool 11 9 240 . Tightening torque 11 42 1AZ. Graphic without reinforcement plate. |
| --- | --- |

|  | Loosen transmission end screw (1). |
| --- | --- |

|  | Attention: risk of damage to four-wheel drive oil sump. Release screws in sequence 27 to 3. Risk of damage!: For safety, hold the oil sump with a second person. Release screws 1 and 2 and remove the oil sump. |
| --- | --- |

|  | Place a drop of sealing compound 2.1 on all the separation points on the crankcase. |
| --- | --- |

|  | Installation note: Special tool 11 8 780 is only necessary if transmission is removed. Position the special tool 11 8 780 with the transmission bolts (1) so that the oil sump is lined up with the engine block. Attach upper oil sump section. (Graphic N47). |
| --- | --- |

|  | Installation note: Rear-wheel drive Clean gasket debris from sealing surfaces with special tool 11 4 470 . Clean all threads with a screw tap. Order number 81 43 0 402 559 Renew gasket. Remount oil pressure switch if replacing oil sump. Join the oil sump with a second persons, apply screws 1 and 2 without microencapsulation M8x28 with 5 Nm. |
| --- | --- |

|  | On the transmission end, screw all the screws (1) with 5 Nm. |
| --- | --- |

|  | Installation note: Four-wheel drive Fasten all the screws in the order 3 to 25 with 27 Nm. Secure screws 26 and 27 with 10 Nm. Exchange screws 1 and 2 with a microencapsulated screw and fasten with 27 Nm. Retourque all screws in order 1 to 27 with 27 Nm. |
| --- | --- |

|  | Secure all screws (1) to their corresponding tightening torque. Tightening torque: 24 00 1AZ. Tightening torque: 23 00 1AZ. |
| --- | --- |

|  | Assemble engine. |
| --- | --- |

Sponsored links

For informational purposes only. Disclaimer>>

|  | Message not specified. |  |
| --- | --- | --- |